Table of Contents

Section I.	Authority	……………………………………………………	pg.   3

Section II.	Purpose	……………………………………………………	pg.   3

Section III.	Definitions	……………………………………………………	pg.   4

Section IV.	Platting Procedure	……………………………………………	pg.   9

4.01	Plat Required …………………………..………………	pg.   9

4.02	Pre-Application Conference …………...………………	pg.  10

4.03	Submissions Subject to Determination of Completeness	pg.  10

Section V.	Preliminary Plats ….………………….………………………… 	pg.  12

5.01	Submission ………………….…………..………………	pg.  12

5.02	Submissions Subject to Determination of Completeness	pg.  13

Section VI.	Final Plats	……………………………………….……………	pg.  17

6.01	Final Plat Procedure and Submission …………………	pg.  17

Section VII.	Construction Plans …………………………………….…………	pg.  19

7.01	Submissions ……………………………………………….	pg.  19

Section VIII.	Construction and Maintenance Bonds …………………………	pg.  22

8.01	Bonds Required …………………………………………	pg.  22

Section IX.	Subdivision Standards and Specifications	……………………	pg.  24

9.01	General Requirements ………………………………….	pg.  24

9.02	Streets or Roads	……………………………………	pg.  25

9.03	Streets in Single Family Lot Districts with Lots less

than 1.5 acres each	……………………………………	pg.  27

9.04	Streets in Single Family Lot Districts with Lots greater

than or equal to 1.5 acres each …………………………	pg.  28

9.05	Easements …	……………………………………………	pg.  29

9.06	Water Utilities …….	……………………………………	pg.  30

9.07	Sewer Utilities ……..	……………………………………	pg.  31

9.08	Lots ...	……………………………………………………	pg.  34

9.09	Floodplains ...……………………………………………	pg.  35

Section X.	Variances ………………………….	……………………………	pg.  36

Appendix A.	Plat Notes for County Officials ….………………………………	pg.  37

Appendix B.	Road Cross Section Concrete …….	……………………………	pg.  39

Cottonwood Subdivision Regulations

SECTION I

Authority

These regulations are adopted under the authority of the Constitution and the laws governing the State of Texas.

SECTION II

Purpose/Applicability

2.01.	Purpose:

- These regulations are to promote and provide for the health, safety, morals, and general welfare of the City, and the safe, orderly, and healthful development of the land in the City limits and ETJ.

- These regulations are to ensure the establishment of rules and guidelines for the Subdivision of property, and to ensure that newly created parcels of land conform to legal statutes.

- These regulations are intended to prevent the City from being burdened with substandard Streets and Roadways in the future, thereby protecting the taxpayers from unnecessary maintenance costs.

- These regulations are to ensure that during the development process, the residents of Cottonwood receive from developers or other stakeholders the necessary services for the supply of water, and that new development will be served by adequate sewage treatment systems and drainage facilities.

- These regulations are intended to provide guidelines for the Subdivision and development of land, and the preparation of Plats and approvals of future development.

2.02.	Applicability:

The rules and regulations contained herein are hereby adopted as the Subdivision Ordinance of the City of Cottonwood, Texas, also cited as “Cottonwood Subdivision Regulations”, and shall be applicable to land within the corporate limits of the City of Cottonwood, as those corporate limits may be from time to time adjusted by annexation or dis-annexation, and within all the area of the extraterritorial jurisdiction of the City of Cottonwood, as that area may exist from time to time as provided by state law, including without limitation Chapter 42 of the Texas Local Government Code.  The City shall have

all remedies and rights provided by state law, including without limitation, Chapter 212 of the Texas Local Government Code regarding the control and approval of Subdivisions and development of land within the City limits and with the City’s extraterritorial jurisdiction.  No person shall subdivide or Plat any tract of land within the City or the extraterritorial jurisdiction of the City except in conformity with these Cottonwood Subdivision Regulations.

SECTION III

Definitions

ALLEY – a minor public right-of-way which is used primarily for vehicular service access to the back or sides of properties otherwise abutting on a Street and not intended to provide the primary means of access to abutting Lots.

BUILDING SETBACK LINE – the line within a property defining the minimum horizontal distance between a building or other structure and the adjacent Street, Right Of Way, or property line and in which no structure shall be located.

CITY – City of Cottonwood, together with its City Council and other operating bodies.

CITY COUNCIL – City Council of the City of Cottonwood, Texas

CITY REPRESENTATIVE – any person designated by the City of Cottonwood to administer or perform duties related to the administration of these Subdivision Regulations, including without limitation, receiving and evaluating applications, and performing inspections, and such person’s designee, including without limitation third party contractors and Engineers retained by City.

COMMISSIONERS COURT – the Kaufman County Commissioners Court.

COMMUNICATIONS SERVICE PROVIDER or CSP - a service provider that transports information electronically, for example a telecommunications service provider. The term encompasses public and private companies in the telecom (landline and wireless), Internet, cable, satellite, and managed services businesses.

COUNTY FLOODPLAIN REGULATIONS – a Floodplain management regulation adopted by Kaufman County in accordance with authorizing statutes.

CUL-DE-SAC – a Street or Road having one outlet to another Street with a vehicular turnaround at the remaining end.

DEVELOPER – any Owner of property who wishes to divide it into more than two or more smaller tracts, including persons, corporations, organizations, estates, trusts, partnerships, agents, associates, and other entities which undertake the activities covered by these regulations.

DRAINAGE PLAN – calculations and drawings showing the existing watershed characteristics and site water flow conditions, and the effects the proposed Subdivision will have onsite and offsite to adjacent and surrounding land prepared as required by City and meeting the requirements of these Subdivision Regulations.

EASEMENT – a right given by the owner of a parcel of land to another person, public agency, or private corporation for specific and limited use of that parcel or a portion thereof authorizing limited and restricted use of such parcel, including the right to ingress and egress.

ENGINEER – any person registered and currently licensed to practice engineering by the Texas State Board of Registration for Professional Engineers or successor agency.

EXCEPTION – a variation or deviation from approved standards, rules, or regulations.

EXTRATERRITORIAL JURISDICTION (ETJ) – that area outside of, but adjacent and contiguous to, the corporate limits of the City of Cottonwood and/or as recognized by state statute as being within the jurisdiction of the City, based on City type and population, where the City is authorized to enforce its’ Subdivision rules and regulations as well as other regulations as allowed by law.

FLOOD INSURANCE RATE MAP – an official map of a community, on which the Federal Emergency Management Administration (FEMA) has delineated both the areas of special flood hazards and the risk premium zones applicable to a community.

FLOODPLAIN – Generally, any land area susceptible to being inundated by floodwaters.  Specifically, the relatively flat or lowland area adjoining a river, stream, watercourse, lake, or other body of standing water, which has been or may be covered temporarily by flood water. Floodplains are typically assigned a recurrence interval (i.e., the 100-year Floodplain) which defines the magnitude of the flood event that causes the inundation. The 100-year Floodplain is the area subject to flood for the 100-year flood.

FLOODPLAIN, 100 YEAR – any area susceptible to inundation by flood waters from any source and subject to the statistical 100-year (has a 1% chance of flooding in any given year).

FLOODWAY – the channel of a river or other watercourse, and the adjacent areas, within a portion of the 100-year Floodplain, that must be preserved in order to discharge the 100-year flood without cumulatively increasing the water surface elevation more than

one foot above the 100-year flood elevation before encroachment in the 100-year Floodplain.

GENERAL RETAIL AND INDUSTRIAL DISTRICT - a district for the conduct of retail trade, including the customary secondary uses, and including wholesale trade or other general business uses, including light manufacturing processes, industrial servicing, or storage processes, in accordance with the Subdivision Zoning Ordinance.

Kaufman COUNTY OR COUNTY – Kaufman County, Texas.

Kaufman COUNTY REGULATIONS – orders and regulations adopted by Kaufman County as authorized by state law.

LOT – a distinct and separate tract or parcel of land being a part of a larger tract of land and having frontage on a Street or Road which is then, or in the future may be, offered for sale, conveyance, transfer, or improved separately from the remainder of any part of the larger tract, and generally intended to be occupied by one building or a group of buildings.

LOT, FLAG-SHAPED OR PANHANDLE – “Panhandle” or “flag-shaped Lot” means an irregularly shaped Lot designed to provide a minimum avenue of Road access while allowing other Lots to be stacked around it creating a narrow strip of land connecting the principal building site to a public or private Street so that the result is a Lot often shaped something like a flag with a “flag pole” of access stretching out to the nearest Road.

ON-SITE SEWAGE FACILITY (OSSF) – all systems and methods used for the disposal of sewage and wastewater on a specific site other than an organized disposal system operated under a valid TCEQ permit.

ON-SITE SEWAGE FACILITY ZONE (OSSFZ) - zone identified for OSSF system.  This area is to meet TCEQ OSSF TAC chapter 287, Table 10 separation distances, which area does not contain Floodplain, structures or any other barriers that would hinder or prohibit proper function of the system.

OWNER – the owner of real property subject to a proposed or existing Subdivision.

PAVED OR PAVING – any reference to paving in these Subdivision Regulations shall mean concrete paving meeting the requirements of this Ordinance.

PLAT – a map depicting the division or Subdivisions of land into, Lots, blocks, parcels, tracts, or other portions.  A Re-Plat shall be considered a Plat for purposes of compliance with these Subdivision Regulations.

PLAT, FINAL – The one official and authentic map of any given Subdivision of land prepared from actual field measurement and staking of all identifiable points by a Surveyor or Engineer, with the Subdivision location referenced to a survey corner, and with all boundaries, corners and curves of the land division sufficiently described so that they can be reproduced without additional references, which depicts the intended development of a property in compliance with all applicable regulations, including without limitation, these regulations and the City’s Zoning Ordinance, as prepared in a form suitable for filing in the County records.

PLAT, PRELIMINARY – one or more drawings showing the physical conditions of a tract of land and the surrounding area intended to be subdivided which depicts a Developer’s intended development program in compliance with all applicable regulations, including without limitation, these regulations, and the City’s Zoning Ordinance.

REGULATIONS – refers to the City of Cottonwood Subdivision Regulations.

REPLAT – any map, drawing, or plan to show further Subdivision or revision of any part of a previously platted Subdivision, addition, Lot, tract, or parcel of land which had been recorded of record in the County Plat records and which may be in either Preliminary Plat or Final Plat form.

REVISION – any map, drawing, or plan to show the revising of any part of a previously platted Subdivision, addition, Lot, tract, or parcel of land which had been recorded as a Final Plat.

RIGHT OF WAY – generally, the entire platted, deeded, or dedicated Public Street or alley which exists between two property lines, whether improved or not, but may also refer to any other public way or portion thereof.  In some instances, the term “Right Of Way” may describe property for public use through prescriptive rights as identified or limited by legal precedent in the State of Texas.  The term may include other facilities and utilities such as sidewalks, parkways and medians, railroad crossings, electrical, communication, oil and/or gas facilities; water or sanitary/storm sewer facilities; or for any other special use.

SHALL – mandatory and not discretionary.

SINGLE FAMILY LOT DISTRICT - primarily a district for single-family detached dwellings on large Lots having a minimum area of five (5) acres and including customary secondary uses in accordance with the Cottonwood Zoning Ordinance.

SPECIAL FLOOD HAZARD AREA (SFHA) – the land in the Floodplain within a community subject to a one percent or greater chance of flooding in any given year according to the Flood Insurance Rate Map.

25-YEAR STORM FREQUENCY - a storm event with a four (4) percent chance of being equaled or exceeded in any given year. Defined in general to be 5.5 inches in 24 hours.

STREET, ARTERY OR ARTERIAL – a Street or Road that will serve vehicular traffic beyond the limits of the Subdivision, connecting Subdivisions with General Retail and Industrial uses or districts, schools, different cities, or remote areas or which serves as a principal connecting Street with State or Federal highways, farm to market Roads or

major thoroughfares shown or projected on current transportation plans of the Texas Department of Transportation.

STREET, COLLECTOR – a Street or Road which connects thoroughfare or Arterial Streets with a Local Street.

STREET, LOCAL – a Street or Road that primarily provides direct access to Lots within a Subdivision.

STREET(S) OR ROAD(S) – as used in these Subdivision Regulations, the term includes a Local Street, Perimeter Street or Road, Private Street or Road, Public Street or Road, County Street or Road, Arterial Street, Collector Street, or any other Street classification.

STREET OR ROAD, COUNTY – a public Street or Road which has been accepted for maintenance purposes by the Kaufman County Commissioners Court, whether acquired by prescription, dedication, or statutory means, or originally constructed by the County.  The term “Street” and “Road” are used interchangeably for the purpose of these Regulations.

STREET or ROAD, PERIMETER – a Street or Road which either exists or will be created wherein a Subdivision as herein defined is partially bounded on one or more sides by such Street or Road and/or where this type of Street has or will have a common frontage along adjoining property which is not a part of the land being considered for platting or Subdivisions.

STREET OR ROAD, PRIVATE – Right Of Way and Roadways that are located within a Subdivision and which are owned and maintained by private parties, a Homeowners

Association, or other non-public entity, are not dedicated to the public, are open for use by the traveling public or are restricted to use by only persons residing with a Subdivision

and for which neither the City of Cottonwood of have County have no maintenance obligations.

STREET or ROAD, PUBLIC – any area, parcel, or strip of land which provides vehicular access to adjacent property or land whether designated as a Street, Road, avenue, lane, thoroughfare, boulevard, place, drive, court, loop, or however otherwise designated, and which is either dedicated or granted for public purposes or acquired for public use by prescription.

SUBDIVISION – the division of any tract or parcel of land into two or more parts to lay out any division of the tract, including an addition, Lots, or Streets, Alleys, squares, parks, or other parts of the tract intended to be dedicated to the public use or for the use of purchasers or owners of Lots fronting on or adjacent to the Street, Alleys, squares, parks, or other parts.  A division includes a division using metes and bounds description in a deed of conveyance or in a contract for deed, by using a contract for sale or other

executory contract to convey, or by using any other method.  As used in this Ordinance, the term may also refer to a development.

SUBDIVISION REGULATIONS or REGULATIONS – the adopted Subdivision Regulations of the City of Cottonwood, Texas, as amended from time to time.

SURVEYOR – a person licensed to practice surveying by the Texas Board of Professional Land Surveying.

TCEQ – the Texas Commission on Environmental Quality, and any successor agency.

TRACT, PARENT – the original land tract owned by the developer prior to any Subdivision.

TRACT, SUBDIVIDED – any of the tracts created by the Subdivision of a parent tract and including the remaining part of the parent tract.

USABLE AREA – the area of land, excluding Floodplain, structures or any other barriers that would hinder or prohibit proper function of an On-Site Sewage Facility or related portion of the system.

SECTION IV

Platting Procedure

4.01	Plat Required:

4.01.01	The owner of a tract of land located within Kaufman County, and inside the corporate limits or ETJ of City of Cottonwood, shall have a Plat of the Subdivision prepared if the owner divides a tract into two or more parts to lay out:

  - a Subdivision of the tract, including an addition to the City;

  - suburban, building, or other Lots; or

  - Streets, Alleys, squares, parks or other parts of the tract intended to be dedicated public use, or for the purchasers or owners of Lots fronting on or adjacent to the Streets, squares, parks, or other parts.

4.01.02	A division of a tract under Section 4.01 includes a division regardless of whether it is made by using a metes and bounds description in a deed conveyance, or in a contract for a deed, or by using a contract of sale, or other executory contract to convey, or by the use of any other method.

4.01.03	The only Exceptions to the requirement that a Plat be prepared shall be those provided in the Texas Local Government Code 212.0045(a) of the Texas Local Government Code for a division of land into parts greater than five (5) acres, where each part has access and no public improvement is being dedicated, or as otherwise provided by law.

4.01.04	Persons subdividing land in the incorporated portions and ETJ of the City of Cottonwood shall comply with all requirements of this Section for Plat approval.  No grading of Streets/Roads or the sale of Lots shall commence, nor shall any other associated construction be accomplished by the Developer upon land being subdivided prior to Final Plat approval, except by written authorization of the City Council.  Approval from the City Council is required before recording a Final Plat.

4.02.	Pre-Application Conference:

A pre-application conference is voluntary but strongly encouraged.   It is recommenced that at least ten (10) days prior to the submission of any application for the Subdivision of

land and official submittal of a Plat for review, a Developer seeking to subdivide land and/or his/her agent (collectively “Developer”) shall schedule a meeting with the City

Representative to discuss filing the requirements of the Cottonwood Subdivision Regulations.

4.03	Submissions Subject to Determination of Completeness:

4.03.01	Applicability The following procedures shall apply to any Subdivision related plan or Application that is required by the City and is submitted in accordance with these Subdivision Regulations.

4.03.02	Determination of Completeness for Subdivision Related Applications Every Required Application shall be subject to a determination of completeness by the City Representative responsible for processing the Application.

1.	Acceptance Standards. The Application shall only be accepted by the City for processing when it is accompanied by all documents required by, and prepared in accordance with, the requirements of these Subdivision Regulations. A typographical error shall not, by itself, constitute an incomplete Application.

2.	Acceptance Procedures. A determination of completeness of an Application shall be conducted in accordance with the following procedures:

a.	A determination of completeness shall be made by the City Representative not later than the tenth (10th ) business day, unless otherwise specified, after the receipt of an Application.

b.	If the submitted Application is incomplete, then the Applicant shall be notified in writing not later than the tenth (10th ) business day after the date of submission of the Application.

i.	Such notice shall be served by depositing it in the U.S. Postal Service, or by electronic mail transmission, before the tenth (10th) business day following submission of the Application.

ii.	The notification shall specify the documents or other information needed to complete the Application and shall state the date the Application will expire if the documents or other information are not provided to the City.

c.      An Application shall be deemed complete on the eleventh (11th) business day after the Application has been received if notice is not served in accordance with this Section.

- If the Application is determined to be complete, the Application shall be processed as prescribed by these Subdivision Regulations.

- Acceptance shall not constitute compliance with these Subdivision Regulations.

- A determination of completeness shall not constitute a determination of compliance with the substantive requirements of these Subdivision Regulations.

4.	Acceptance shall not Guarantee Approval. There is no implied intent or guarantee that an accepted and completed Application will be approved, if after the Application is deemed complete, it is determined that the Application does not comply with these Subdivision Regulations.

4.03.03	Re-Submittal after Notification of Incompleteness

1.	If the Application is re-submitted after a notification of incompleteness, the Application shall be processed upon receipt of the re-submittal.

2.	The statutory 30-day time frame for Plat approvals shall begin on the date of the re-submittal.

3.	To the extent that the information or documents submitted is not sufficient to enable the City Representative to apply the criteria for approval, the Application may be denied on such grounds.

4.03.04	Waiver of Right to 30-Day Action. The designated City Representative shall be the Responsible Official to approve a Waiver of Right to 30-Day Action.

1.	Request. An Applicant may submit in writing a Waiver of Right to 30-Day Action.

2.	Received.

a.	If the Applicant is requesting a Waiver of Right to 30-Day Action, the Waiver of Right to 30-Day Action must be received by the City Representative on or before the seventh (7 th ) calendar day prior to the meeting at which action would have to be taken (based on the 30-day requirement in State law) on the Application.

b.	Waiver requests that are not received by that day shall not be considered properly submitted, and action shall be taken on the Application at such meeting as scheduled.

3.	Requirements Maintained.

a.	Submission of a Waiver of Right to 30-Day Action, and acceptance of such waiver by the City as part of an Application, shall not be deemed in any way a waiver to any requirement within these Subdivision Regulations.

4.03.05	Expiration of a Subdivision Related Application Before a decision of approval pursuant to the Texas Local Government Code Chapter 245, a Subdivision related Application shall automatically expire (ending all vesting claims) at the close of business on the forty-fifth (45th) calendar day after the date of Application submission, if:

1.	The Applicant fails to provide documents or other information necessary to comply with the City's technical requirements relating to the form and content of the permit Application;

2.	The City provides to the Applicant, not later than the tenth (10th) business day after the date the Application is filed, written notice that specifies the necessary documents or other information, and the date the Application will expire if the documents or other information is not provided; and

3.	The Applicant fails to provide the specified documents or other information necessary to comply with the City's requirements relating to the Application within the time provided in the notification.

Section V.

Preliminary Plats

  - Submission:

5.01.01	The submission of a Preliminary Plat is necessary to:

    - eliminate the duplication of Subdivision names and Street names;

    - assure proper alignments of Streets and drainage facilities;

    - assure that the provisions of the applicable Floodplain Regulations will be complied with, and that no Lot will have a drainage problem;

    - assure that the provisions of Kaufman County Sewage Regulations will be complied with;

    - assure that all necessary permits or plan approvals have been or will be procured;

    - assure compliance with all applicable ordinances of the City.

5.01.02	The Developer shall submit five (5) copies of a Preliminary Plat, a Plat application form, required supporting documents, and applicable Plat review fees to the City Secretary for the City prior to being added to the regular meeting agenda.  Preliminary Plat applications which do not include required information and documentation shall be considered incomplete, and in accordance with state law and Section 4, shall be returned to the Developer. Additional copies of the Preliminary Plat may be required if revisions or corrections are necessary.  A Preliminary Plat shall include all contiguous property under the ownership or control of the Developer and may contain more than one (1) phase provided that each phase is clearly identified.

5.01.03	In no event shall a Preliminary Plat be submitted to the City Council later than fourteen (14) days prior to the date for the posting of the City Council agenda for the meeting at which the approval of the City Council is requested.  Unless the City Council takes action stating otherwise, an approved Preliminary Plat will remain valid for a period of twelve (12) months from the date it is approved, after which time it will automatically become void.  All fees paid on a voided Preliminary Plat shall be non-refundable.)

5.01.04	Prior to presenting a Plat to the City Council for Preliminary approval, the Developer shall deliver a copy of the Plat to (1) the Kaufman County Sanitarian for his/her review for compliance with sewage disposal regulations and (2) to the Kaufman  County 911 Coordinator for review for compliance with Kaufman County 911 addressing requirements.  Developer shall provide City with a document evidencing Kaufman County’s review and approval of the proposed plan for sewage disposal and review and

approval of the proposed addressing.  Failure to comply with the requirements of this Section shall cause a Plat application to be deemed incomplete.

5.01.05	After review of a Plat application, the City Representative shall notify the Developer in writing of any necessary corrections to the Plat in accordance with

  - Submissions Subject to Determination of Completeness:

5.02.01	Upon receipt of a completed application, the Preliminary Plat application shall be placed on the City Council agenda. City Council approval shall be required before the Developer may proceed with Final Plat submittal and approval.

5.02.02	If the property subject to the proposed Plat is located within the City of Cottonwood and/or the extraterritorial jurisdiction of the City, the Developer shall be responsible for complying with these Regulations and all ordinances of the City, as applicable, and/or the provisions of any applicable interlocal agreement governing Subdivision and development of property in the ETJ, as applicable.  In the event that these Regulations differ from regulations adopted by Kaufman County, the more restrictive regulation shall control and shall be enforced by City unless expressly waived by the City Council.

5.02.03	Preliminary Plat approval by the Cottonwood City Council does not constitute acceptance of the Subdivision.  It only authorizes the Developer to proceed with preparation of the Final Plat.  No grading of Streets or construction is authorized in a Subdivision before approval of the Final Plat by the City Council, except as otherwise approved by the Council. An approved Preliminary Plat shall be valid for twelve (12) months from the date of City Council approval unless City Council expressly provides otherwise.  If a Final Plat is not submitted to the City Council for approval within that period of time, the Developer shall be required to submit a new Preliminary Plat with all applicable fees and supporting documents for approval prior to City Council’s consideration of a Final Plat.

    - Each Preliminary Plat submission shall include the following:

- Preliminary Plats shall be drawn on a 24” X 36” sheet, scale not to exceed 1” = 200’.

- Name, address, and telephone number of the owner, Surveyor, and/or Engineer.

- The seal and signature of the Surveyor and/or Engineer responsible for the preparation of the Plat.

- The proposed name of the Subdivision and the names, locations, width, and dimensions of all proposed and existing Streets, Alleys, Easements, parks and other public places, Lot lines, and proposed land uses.  No proposed name shall conflict with any other Subdivision or Street in the City of Cottonwood or Kaufman County, or any other adjacent Subdivision.  Conflict shall be determined at the discretion of the City and in accordance with the Kaufman County 911 addressing regulations.

- The location of the existing boundary lines of the Subdivision and total acreage including the estimated acreage of each Lot.

- On a Plat for land less than one and one half (1.5) acres, all pad and building sites for each Lot will also be shown on Plat.

- A vicinity map showing the Subdivision location within the County and the relationship to the nearest existing Roads and municipality.

- The date the Plat was prepared.

- Scale, and North directional arrow.

- The location of the 100-year Floodplain, as defined by FEMA maps and the identification of all Lots, or any part of a Lot, that is located within the

- 100-year Floodplain.  For Subdivisions containing a Floodplain, a note on the Plat stating the following is required:

  - A Development Permit shall be required from Kaufman County prior to any construction within the Floodplain.”

  - The finished floor elevations shall be shown for each Lot located in the Floodplain at two (2) feet above the Basic Flood Elevation (BFE).  If no part of the Subdivision lies within the 100-year Floodplain, then it shall be so noted.

- The Preliminary Plat shall include a Drainage Plan prepared by a Texas Licensed Professional Engineer and provided in a form acceptable to City

- Representative.  The Preliminary Plat shall show the 100-year flood plain elevation and boundaries, existing bridges, culverts and other drainage structures, and physical features of the property that is the subject of the Subdivision related to Street and Lot drainage and layout.  The Drainage Plan shall show existing drainage areas upstream and downstream including drainage calculations determining the quantity to run off coming by means of land, entering, crossing and exiting the proposed Subdivision.  The drainage calculations shall be sufficiently detailed to determine changes in the 100-year flood plain elevation, water discharge and velocities within the Subdivision and upstream and downstream of the Subdivision, and both pre-construction and post construction Runoff values and means of mitigating any increased runoff.

- Topography of the development shall be shown on the Preliminary Plat.  Pre-construction and post construction contour intervals shall be shown

for assessment and determination of proper drainage requirements.  The intervals shall be as follows: 1) Land with less than five percent (5%) overall slope, the contour interval shall not be greater than two (2) feet.  2) Land with more than five percent (5%) slope, the contour interval shall not be greater than five (5) feet.

- The name of all adjacent property owners with the volume and page of recordation, and any adjacent Subdivisions and Streets including how the Streets in the proposed Subdivision may connect with other Streets in the area.

- Description, location, and dimensions of any and all proposed and existing utility, drainage, and pipeline Easements within and adjacent to the proposed Subdivision, with applicable recordation, shall be visible and apparent.  Enclosed pipe requires a minimum twenty foot (20)’ Easement width.

- All Easements shall be so designed to allow maintenance equipment to enter the Easement and be able to perform the necessary work.

- All maintenance responsibilities, whether private or by Kaufman County, shall be noted on the Plat with the party responsible for such maintenance clearly designated.

- Preliminary water and sewer plans, if applicable.

- The name of the water, sewer, Communication Service Provider and electric utility companies providing service to the Subdivision shall be noted on the Plat.  A statement shall be provided if sewage disposal is by individual on-site sewage facilities and/or water service by individual wells.

- A certification letter from the water, sewer, Communication Service Provider and electric utility companies guaranteeing their intent to provide service to the proposed Subdivision and providing a time frame and cost estimate for the establishment of these services when applicable, shall be included with the application.

- A certification letter evidencing Kaufman County’s review and approval of the proposed plan for sewage disposal and review and approval of the proposed addressing.

- For a Subdivision proposing to use on-site septic systems for sewage treatment, the Developer shall comply with all requirements of Kaufman County relative to approval of such on-site septic system.  The minimum Lot size is (1) acre per Lot pursuant to the Kaufman County On-Site Sewage Facility Regulations. Lots utilizing on-site sewage facilities shall provide for a minimum of one (1) acre Useable Surface Area. This area excludes ponds/lakes and Easements provided one half (0.5) of one acre of the property is exclusively designated and platted as “On Site Sewage Facility Zone

- For Subdivisions with the minimum 1-acre Lot size all OSSF disposal field sites shall be noted as no build sites on Plat.

- For Subdivisions proposing individual water wells for water service, an Engineer’s report shall be required to certify that an adequate supply of groundwater exists to serve the proposed Subdivision as required by

- County regulations.  The report shall also clearly illustrate any existing OSSF systems within two hundred (200’) of the proposed Subdivision.

- If the proposed Subdivision is a portion of a larger tract, which to further subdivided at a later time in phases, a master plan of the Subdivision in

its’ entirety shall be submitted with the Preliminary Plat of the first phase        of the proposed Subdivision.

- Notwithstanding the foregoing, the Developer shall provide additional forms, contracts, plans, certifications, and any other supplementary documents deemed necessary for the evaluation of an application and the enforcement of these Regulations by the City.

Section VI.

Final Plats

6.01	Final Plat Procedure and Submission:

The Final Plat procedure and the procedure for a Replat shall be the same as that for the Preliminary Plat except as noted in these Regulations.  Approval of the Preliminary Plat is required prior to submission a Final Plat by Developer.  City Council approval of the Final Plat and recording of the Plat shall be a condition precedent to the sale of any Lot within the Subdivision or the issuance of any building or other permit for work within the Subdivision.  The Final Plat shall be recorded with the County Clerk within ninety (90) days of City Council approval.  A single ninety (90) day extension may be granted by the

Council by official action.  Final Plat approval shall not be construed as conferring acceptance of Streets or Roads by the City for any purpose, or by the County for maintenance purposes.

6.01.01	Final Plats shall contain and be accompanied by the following information:

- Final Plats will be drawn on 18” X 24” sheets at a scale not to exceed 1” = 200’.  Seven (7) blue line copies of the Final Plat together with two (2) Mylar sheet copies are required.

- Final Plats shall show the information required by this Section, and as approved the City Council for the Preliminary Plat.

- A completed application form, and the appropriate Plat review fees.

- Three (3) sets of construction plans sealed by a licensed Engineer.

- Cost documents prepared by the Developer’s Engineer or contractor for the construction of Streets, drainage structures, utilities, and all other improvements.

- Construction bonds for Street and drainage improvements.

- An original tax certificate from the Tax Collector of each political Subdivision in which the property is located to certify that no delinquent taxes are due on the proposed Subdivision.

- A signature block for approval of the Mayor and City Secretary attestation to file the Plat for record with Kaufman County.

- A dedication, by the Developer, of all Streets, Roadways, Alleys, utility Easements, and other land intended for public use, and the owners’ certification that all parties with any interest in the title to the subject property have joined in such dedication, duly executed, acknowledged, and sworn to by said owner before a notary public.

- The following requirements shall apply to each Plat approved pursuant to these Regulations, and the following statements evidencing these requirements shall appear on every Plat containing private Streets, drives, emergency access Easements, recreation areas, and open spaces:

  - All private Streets, Roads and drives shall be designated as private with signage that clearly identifies each such Street, Road or drive as having private status.

  - CITY OF COTTONWOOD SHALL NOT BE RESPONSIBLE FOR MAINTENANCE OF PRIVATE STREETS, DRIVES, EMERGENCY ACCESS EASEMENTS, RECREATION AREAS, COMMON AREAS AND/OR OPEN SPACES OR OTHER SIMILAR AREAS (COLLECTIVELY “PRIVATE AREAS”).  THE OWNERS OF SUCH PRIVATE AREAS SHALL BE RESPONSIBLE FOR THEIR MAINTENANCE; SUCH OWNERS AGREE TO RELEASE, DEFEND, INDEMNIFY AND HOLD HARMLESS CITY OF COTTONWOOD, ITS OFFICERS AND EMPLOYEES, FROM ALL CLAIMS, DAMAGES, AND LOSSES ARISING OUT OF OR RESULTING FROM THE PERFORMANCE OF THE OBLIGATIONS OF SAID OWNERS SET FORTH IN THIS PARAGRAPH.

- The seal and signature of the Surveyor or Engineer responsible for preparation of the Plat, and the date the Plat was prepared.

- A legal description of the property and location with respect to an original corner of the parent tract.  Total acreage shall be noted.

The number of all Lots and blocks arranged in a systematic order.  The names of all Streets.  The curves on all Streets, blocks, Lots and easements shall include the

radius, length, and central angle of the curve.  Lots will show area in acreage or square feet.

- The accurate location of adjacent Subdivision Streets, blocks, Lots, and Easements, or note that the adjacent property is undeveloped.

- A copy of the Subdivision restrictions, if any, shall be properly signed and notarized and filed for record with the County Clerk.

- The location, size, and description of all permanent monuments and control points.

- The following regulations shall apply to each Plat approved pursuant to these Subdivision Regulations and the following statements shall be noted on each approved Final Plat:

  - Blocking the flow of water or construction improvements in drainage Easements, and filling or obstruction of the Floodway is prohibited.

  - The existing creeks or drainage channels traversing along or across the subdivided tracts will remain as open channels and will be maintained by the individual owners of the Lot or Lots that are traversed by or adjacent to the creeks or drainage channels.

- The City of Cottonwood will not be responsible for the maintenance and operation of drainage ways for the control of erosion located on private property.

  - The City of Cottonwood will not be responsible for any property damage, property loss, personal injury, or loss of life by flooding or flooding conditions.

All surface drainage Easements shall be kept clear of fences, buildings, foundations and planting, and other obstructions to the operation and maintenance of the drainage facility.

  - Construction not completed within two (2) years of the recording date shall be subject to the current constructions’ standards, as applicable.

6.01.02  The City Council of Co shall have the authority to refuse to approve or authorize any map or Plat of any such Subdivision, unless such map or Plat meets the requirements as set forth in these Regulations.

6.01.03  A public hearing and public notices shall be required for a residential replat in accordance with the Texas Local Government Code, as amended from time to time.

Section VII.

Construction Plans

7.01	Submissions:

All construction plans, drawings, and calculations required under these Subdivision Regulations shall be sealed by a Registered Professional Engineer licensed to practice in the State of Texas.

    - Three (3) sets of all construction plans (18” X 24” sheets) must be submitted to and receive approval from the City Council, unless a variance is granted, prior to the commencement of any construction in accordance with Section 10 of these Regulations.

    - All Construction Plans shall be submitted with the Final Plat.

    - Construction Plans shall be reviewed by the City Representative or their designee, and one set of approved plans will be returned to the Developer.  Developer shall be notified of required corrections or additions.

    - Construction Plans must be approved prior to the approval of the Final Plat by City Council.

    - Construction Plans shall consist of:

- Street plans;

- Drainage Plans;

- Water, electric, communications service or and sewer system, if any; and,

- Location and description of all Easements.

7.01.06	Street construction plans shall include the following:

- Title sheet showing names of Subdivision, developer, Engineer, date and location map.  Include a space for approval by the City Council;

- The plan of the Street at a scale no larger than 1” = 50’, showing the location of the proposed pavement, ditches, and structures within the Street Right Of Way;

- The profile of the Street at no larger than 1” = 50’ horizontal, and 1” = 5’ vertical;

- Both the Street grade and elevation;

- Both the ditch grade and sections;

- Typical Street sections; and

- The seal and signature of the Engineer responsible for the design on all sheets.

7.01.07	Drainage constructions plans shall include the following:

- The plan of the drainage ditches or structures including a ditch profile and typical section view in no larger than a 1” = 50’;

- The ditch grades, design flow of water, design depth of water, design velocity of water, and the direction of flow within Street and drainage channels shall be clearly noted.  The use of existing channels is encouraged;

- A plan and profile of all culverts under any Street with the design flow of water;

- The size of all driveway culverts to carry the design flow of water to each Lot in the Subdivision when the culvert is installed at the designed ditch grade;

- A table containing the size of each pipe shall be included on the Plat.  The developer is responsible for notifying builders and Lot owners of the required culvert size;

- The plans shall include a hydraulic summary table, identify the boundary of the drainage area contributing runoff into the drainage system, and be based on a 25-Year Storm Frequency; and

- The plans shall contain the following statement executed by the Engineer responsible for the design:

I, __________________________, a Texas Licensed Engineer, do hereby affirm that to the best of my knowledge, information, and belief, and based upon the information provided, the drainage improvements shown on these plans will have no adverse effect on any property adjacent to the property shown.

7.01.08	Water construction plans shall show:

- The location and size of all proposed water lines in relation to the Right Of Way, and/or Easements in which the lines are to be located;

- The location of all appurtenances proposed to be installed;

- The minimum cover depth to which the water lines are to be installed shall be no less than 30” (inches); and

- The seal and signature of the Engineer responsible for the design on all sheets.

    - Sewage construction plans shall show:

- The plan of the sewer line in no larger than 1” = 50’ scale, showing the location and size of all proposed sewer lines in relation to the Right Of Way or Easements in which the lines are to be located;

- The location of all appurtenances proposed to be installed;

- The sewer line grades and elevations at all junction points; and

- The seal and signature of the Engineer responsible for the design on all sheets.

    - Fire Suppression System.  Fire Suppression Systems shall comply with all requirements of State law and Kaufman County regulations.  Pursuant to the Texas Local Government Code, as amended, and other applicable law, any Subdivision that is not served by fire hydrants as part of a centralized water system certified by the Texas Commission on Environmental Quality may be required to provide construction plans showing:

- for a Subdivision of fewer than 50 houses, 2,500 gallons of water storage; or

- for a Subdivision of 50 or more houses, 2,500 gallons of water storage with a centralized water system or 5,000 gallons of water storage.

Section VIII.

Construction and Maintenance Bonds

8.01	Bonds Required:

Prior to recording a Final Plat, the following financial securities are required:

    - Construction Performance Bond

- The Developer shall complete all construction of public improvements within two (2) years after approval of Final Plat. The Developer shall obtain and provide to City a Construction Performance Bond with City as beneficiary, executed by a Surety Company authorized to do business in the State of Texas, and made payable to the City of Cottonwood, Texas on a bond form acceptable to the City. The bond shall be subject to the approval of the City.

- The amount of the Construction Performance Bond shall be equal to one hundred percent (100%) of the estimated cost of construction of Roads, Streets, Street signs, underground utilities, required drainage structures, and all other associated public construction improvements based on an estimated cost certified by the Developer or its Engineers and approved by the City Representative. Such bond shall contain a provision requiring the automatic increase in penal sum from the estimated cost of construction to the actual cost of construction due to change orders and/or other increases in the estimated cost of construction.

- The Developer shall submit the Construction Performance Bond with the Final Plat prior to City Council approval of the Final Plat.

- The Construction Performance Bond shall remain in full force, and in effect, until all Roads, Streets, Street signs, underground utilities, required drainage structures, and all other associated construction improvements in the Subdivision have been completed to the satisfaction of the City Council, and the construction has been released by the City Council on the recommendation of City Representative, through official Council action, in accordance with this Section.  To request a release, the Developer shall present a written request to release the bond to the City’s representative.  This request shall contain a statement made by the Engineer responsible for the design of improvements stating that the Engineer has inspected the improvements covered by the bond, has determined that the improvements comply with the applicable design requirements and these Subdivision Regulations and recommends the acceptance of the improvements by the City Council or Kaufman County, as applicable.  Attached to the letter shall be one set of “as built” drawings showing the work to be accepted for

- use by the City. The written request of bond release shall be provided to the City Secretary at least twenty-one (21) days prior to the posting date for the agenda for the next regularly scheduled meeting of the City Council.

- The Developer shall provide written notice to the City Council of the date of substantial completion of all Roads, Streets, Street signs, underground utilities, required drainage structures, and/or all other associated construction improvements in the Subdivision.  If the City Representative or its designee provides written notice to the Developer of any defect in any of the improvements within two (2) years from the date the Council receives the notice of substantial completion for such improvement (“Deficiency Period”), and the Developer fails or refuses to correct the defect within sixty (60) days from the date it receives notice from the City, the defect shall be corrected at the cost and expense of the obligee or financial security. The Construction Performance Bond shall include language encompassing the provisions in this paragraph.  The Construction Performance Bond shall also be written to allow for a claim against the obligor or surety company for one (1) year after the expiration of the 2-year Deficiency Period described in this paragraph.

    - Maintenance Bond

- To ensure Roads, Streets, Street signs, underground utilities, required drainage structures, and all other construction are properly maintained, a maintenance bond shall be provided by Developer with either the City as beneficiary, or at City’s sole discretion, with the County as beneficiary.  The maintenance bond shall be executed by a surety company authorized

- to do business in the State of Texas, on a form acceptable to the City, and made payable to the City of Cottonwood, Texas.   The maintenance bond shall be in a penal sum equal to one hundred percent (100%) of the actual costs of construction of the public improvements and shall be valid for a period of two (2) years from the date of final acceptance of the public improvements by City or County, as applicable.  The maintenance bond shall be provided to City immediately upon final completion of the improvements for which the construction performance bond was provided and shall be subject to the approval of the City Council.

8.01.03	In addition to compliance with these Regulations, Developers shall comply with all Kaufman County regulations applicable to maintenance of County

Roads, including without limitation, compliance with County inspection requirements and related fees.

Section IX.

Subdivision Standards/Specifications

9.01	General Requirements:

- Except as provided herein, no Plat or improvements thereon shall be approved or accepted by the City Council unless it conforms to the minimum standards and specifications contained herein.

- If a tract is subdivided into parcels larger than the minimum Lot requirement for the applicable zoning district or other applicable regulation, such parcels shall be arranged to allow the opening of future Streets.

- There shall be no reserve strips controlling access to land dedicated or intended to be dedicated to public use.

9.02	Streets or Roads:

9.02.01	All Streets and Roads, regardless of type or classification, within a Subdivision submitted for final Plat approval shall be constructed to meet the standards and specifications for Streets or Roads set forth in these Subdivision Regulations and shall comply with North Central Texas Council of Government Standards for Public Works Construction.  In the event of a conflict, the more stringent standards shall apply unless expressly waived by the City Council.   The Developer of a Subdivision shall be

responsible for the cost of construction for all Streets and Roads, drainage, and other improvements, both public and private, within the Subdivision.

9.02.02	Testing shall be performed by a qualified Engineering laboratory, and the cost of all testing shall be the responsibility of the Developer.

9.02.03	The City Council may require that a Subdivision contain additional points of ingress and egress to the Subdivision from a Street or Road for emergency vehicle access, and to provide for increased traffic flow and public safety.

9.02.04	Street or Roads shall be classified, based upon the definitions in Section III, “Definitions” of these Regulations, during the Preliminary Plat review.  The City

Council shall be the final authority for interpretation of level of service and determination of appropriate Road classifications for a Subdivision.

9.02.05	Streets or Roads for Single Family Lot Districts shall meet all NTCOG standards for public works construction and:

- Provide a minimum Right Of Way of sixty (60) feet;

- Meet the Subgrade and Surface requirements set forth in Section 9.03 below;

3.        Provide a minimum paved Road surface of twenty-six (26) feet in width

and a base course of not less than thirty (30) feet in width.

    - Concrete Collector Streets that are used for drainage shall be:

- a minimum Right Of Way width of sixty (60) feet

- a minimum paved Road surface width of thirty-two (32) feet from back of curb to back of curb; and

- a base course of not less than thirty-six (36) feet in width

9.02.07	Main Artery Streets or Roads shall meet the minimum requirements set forth by the Texas Department of Transportation for the level of traffic projected for the proposed Street and the associated service level as determined appropriate by the City Council for the proposed Street.  City may require Developer to provide a traffic impact analysis and/or other information projecting traffic counts and establishing appropriate service levels for proposed Streets.

9.02.08	Cul-De-Sacs shall have:

- a minimum Right Of Way radius of sixty (60) feet:

- a minimum paved Roadway surface radius of forty-five (45) feet in width; and,

- a minimum base course of not less than a forty-seven (47) foot radius.

9.02.09	A Cul-De-Sac that exceeds two thousand five hundred (2,500) feet in length between the center of the turnaround and the intersection of the Cul-De-Sac with another Street or Road may require additional turn around space for emergency personnel as determined necessary by City Council.

9.02.10	Alleys shall have a Right Of Way width of not less than twelve (12) feet.

9.02.11	A proposed Subdivision that adjoins or encompasses an existing Public Street, that does not comply with the minimum Right Of Way requirements of these Regulations, shall provide the dedication of additional Right Of Way along either or both sides of such Street so that the minimum Right Of Way required by these Regulations can be established.  If the proposed Subdivision abuts only one side of such Street, then a minimum of one-half of the required Right Of Way shall be dedicated by the Developer of the Subdivision. Any trees, vegetation and/or fencing that is in the newly dedicated Right Of Way shall be removed by the developer upon Right Of Way dedication and prior to the commencement of development.

9.02.12	All Streets or Roads shall either be connected at both ends to a dedicated Street or shall be provided with a turnaround having a minimum paved radius of forty-five (45) feet, and a minimum Right Of Way radius of sixty (60) feet as provided in these Regulations.

9.02.13	All Streets or Roads, including without limitation associated drainage infrastructure, shall be designed using North Central Texas Council of Government Standards for Public Work Construction and shall be constructed in accordance with the standards therein and in order to handle a minimum twenty-five (25) year flood within the Right Of Way. In the event of a conflict, the more stringent standards shall apply unless expressly waived by the City Council.   Developer shall design and construct drainage improvements such that all excess water shall be carried off by the use of adequate storm drainage structures or ditches.

9.02.14	Streets/Roads, where practical, shall intersect at a ninety (90) degree angle.  Where this is not practical, the intersection, on the side of the acute angle, shall be rounded with a curve or a cut-back, but in no case shall the curve have less than a twenty-five (25) foot radius.

9.02.15	New Streets or Roads which are a continuation of an existing Street or Road shall be a continuation, without offset, of the existing Road.

9.02.16	Where Streets or Roads in an adjoining Subdivision end at the property line of a new Subdivision, the Streets or Roads of the adjoining Subdivision shall be continued throughout the new Subdivision.  Where no adjacent connections are platted, the Roads in a new Subdivision shall be a reasonable projection of the Streets or Roads in the nearest Subdivision.

9.02.17	New Streets or Roads shall be named to provide continuity with existing Streets or Roads in adjacent Subdivisions that may be expected to extend to the proposed Subdivision and shall not be named in such a manner as to create confusion or conflict.  Confusion or conflict shall be determined at the discretion of the City and in accordance with the Kaufman County 911 addressing regulation and shall be resolved at the discretion of the City Council.

9.02.18	No landscaped “islands”, ornamental entrances, trees, decorative squares, or any other obstruction to traffic shall be constructed or preserved within the Right Of Way of a Street or Road dedicated to the public without authorization from the City Council.  If landscaping and/or irrigation is proposed within the Right Of Way, the Developer shall create an organization (homeowners association or property owners association) that will be responsible for the continued maintenance of and liability for the landscaping and/or irrigation system installed for the Subdivision.  The organization shall have assessment authority to insure adequate funding for maintenance.

  - Streets in Single Family Lot Districts with Lots less than 1 acres each:

In addition to compliance with the general standards for Streets, Streets in a Single Family Lot District shall be twenty-six (26) feet in width measured back of curb to back of curb. The provisions of this Section shall control in the event of conflict between this Section and general requirements for Streets.   Collector Streets shall be thirty-two (32) feet in width measured back of curb to back of curb and shall meet the following requirements:

9.03.01	Subgrade - The subgrade shall be lime stabilized with hydrated lime in the amount of 7% by weight of the subgrade to a depth of six (6) inches for the stipulated width, plus one foot behind the curbs.  The City may consider other types of and percentages of lime based on geotechnical laboratory’s tests, evaluations and recommendations described in engineering reports provided such reports are paid for by the Developer.

9.03.02	Surface - The surface course shall be six (6) inches in thickness of 3,600 psi or greater of Portland cement concrete. (See Appendix A – Appendix B).

    - Streets in Single Family Lot Districts with Lots greater than or equal to 5 acres each

In addition to compliance with the general standards for Streets, Streets in a Single Family Lot District with Lots greater than or equal to 5 acres each shall comply with the requirements of this Section; the provisions of this Section shall control in the event of conflict between this Section and general requirements for Streets.  All Streets or Roads shown on a Plat shall be concrete paved at the property line, and shall meet the following minimum requirements:

    - Subgrade - The subgrade shall be lime stabilized with hydrated lime in the amount of 7% by weight of the subgrade to a depth of six (6) inches for the stipulated width, plus one foot behind the curbs.  The City may consider other types of and percentages of lime based on geotechnical laboratory’s tests, evaluations and recommendations described in engineering reports provided such reports are paid for by the Developer.

    - Surface - The surface course shall be six (6) inches in thickness of 3,600 psi or greater of Portland cement concrete. (See Appendix A and Appendix B).

9.04.03	Developer may apply for an Exception to the requirements of these Regulations for the construction of Local Streets or Roads, and the City Council may grant an Exception when:

- the smallest Lot in the Subdivision is ten (10) acres or more in area;

- the Roadway is owned by a homeowners association; and

- the Street or Road is privately maintained.

9.04.04	Private Roads: All Roads in the City of Cottonwood, regardless of zoning district where such Roads are located or Lot size, are to be private Roads unless otherwise expressly designated by the City, County, or State.

- Private Roads, Streets, etc. shall conform to the City of Cottonwood Subdivision Regulations; and,

- Private Streets, Roads, and emergency access Easements shall be termed as a vehicular access way under private ownership and maintenance; and,

- Gated Subdivisions (having security gates or guard stations) are considered privately owned and shall be maintained without any City contribution.  Access passcodes shall be provided to emergency agencies.

9.04.05	On each Final Plat, the Developer shall identify the type of material used or proposed to be used in the construction of each existing Street or Road and each Street or Road proposed to be constructed, expanded, extended, or otherwise altered, pursuant to the Final Plat.

9.04.06	The Developer shall be required to install culverts under Streets at all entrances and at drainage courses as specified by the City Council or applicable engineering specifications.  All culverts shall be constructed of metal or Concrete with a minimum of thirty (30) feet in length at all entrances.

9.04.07	All utilities shall be placed and stubbed out from under the surface of the Street Surface to the Street Right Of Way line so as not to disturb the Road surface during the process of extending and connecting services to each Lot.

9.04.08	No Exception to any provision or these Regulations or exclusion from any requirement in these Regulations shall be allowed unless approved by the City Council after a finding of good cause.  Notwithstanding the foregoing, a finding of good cause shall be at the sole discretion of the City Council.

  - Easements:

9.05.01	Public Utilities Easements. Easements provided for the location of public utilities shall meet the following requirements:

- Be a minimum of fifteen (15) feet in width along the front and rear property line of a Lot, and a minimum of ten (10) feet in width along the side property line of a Lot.  It shall be the responsibility of the Developer to ensure that all utility Easements are of the proper width and are

- properly located to serve the requirements of each utility company providing a service to a Lot.

- When crossing a Street or Road, utilities shall be buried a minimum of twenty-four (24) inches below the ditch line, or a minimum of thirty-six (36) inches below the crown of the Street or Road, whichever is greater.

- If new Streets or Roads are constructed over existing petroleum pipeline crossings, the pipe shall be protected as follows:

  - Encased pipe shall be a minimum of three (3) feet below the deepest proposed ditch line.

  - Non-cased pipe (of extra wall thickness meeting federal regulations) shall be a minimum of four (4) feet below the deepest proposed ditch line.

    - Drainage Utilities Easements. Drainage utilities and Easements for drainage utilities shall meet all requirements of applicable Kaufman County Regulations as well as these Regulations, State and Federal law, and shall comply with any and all requirements of the North Central Texas Council of Governments Standards for Public Works Construction.  In the event of a conflict, the more stringent standards shall apply unless expressly waived by the City Council.   As a condition of Final Plat approval, each Developer of a Subdivision shall provide a letter of authorization/certification from Kaufman County certifying that drainage for the proposed Subdivision complies with all Kaufman County drainage regulations.  Additionally, Developers shall at minimum comply with the following requirements:

- Be dedicated by the owner of sufficient width and location in order to maintain and construct the storm water drainage system based on the plans prepared by a registered professional Engineer and approved by Kaufman County.

- Be located along existing drainage channels, and generally equal the top width of the channel plus ten (10) feet on each side.

- Where drainage crosses a Street or Road, the storm drainage shall be carried in pipe(s) or through bridges or culverts sized by a registered professional Engineer at the Developer’s expense.  Developer shall provide any additional drainage Easements, outside of the Right Of Way and at culvert crossings, as required by the City or Kaufman County for maintenance and/or protection of the County Street/Road System.

  - Water Utilities:

As a condition of Final Plat approval, each Developer of a Subdivision shall provide a letter of authorization/certification from the utility company or companies providing water service to the proposed Subdivision certifying that water service to the proposed Subdivision complies with requirements of the entity providing water service.  Additionally, Developers shall comply with all requirements of applicable Kaufman County Regulations as well as these Regulations, State and Federal law applicable to

water utilities and fire hydrants, and shall at minimum comply with the following requirements:

- In any area of the City or county that potable water is supplied or eligible to be supplied by a potable water supplier, the Developer of a Subdivision shall provide, construct and install all water lines, to insure access to water for each Lot unless a variance is obtained by the Developer and provided to  the City Council and such Variances provides that the potable water supplier has agreed to supply, and has the ability to supply, potable water to all Lots located within the Subdivision.

- Comply with Chapter 341 of the Texas Health and Safety Code, as amended.

- Where drinking water is to be supplied to a Subdivision from a central system, the water quality and system design, construction, and operation shall meet the minimum criteria set forth in 25 TAC Section 337.201-337.212, and 25 TAC 337.1-337.18, as amended from time to time, and other applicable regulations.

- Developers who propose to supply drinking water by connecting to an existing central system shall provide a written agreement with the public water supplier.  The agreement must accommodate the total flow anticipated from the ultimate development and occupancy of the proposed Subdivision.

- Transportation or conveyance of potable water by transport truck or other mobile device to supply domestic needs of the Subdivision shall not be allowed, except in the case of emergency.

- Where water supplies are to be provided by an existing political Subdivision of the state, including a city, municipal utility district, water control and improvement district, nonprofit water supply corporation, special utility district, or an existing investor-owned water supply corporation, the Developer shall furnish a certificate of convenience and necessity evidencing the authority of the political Subdivision to provide

service and shall provide a letter from the political Subdivision certifying that water service will be provided to the Development.

- Before approval of a Final Plat, plans and specifications for the proposed water facilities system shall have been approved by all entities having jurisdiction over the proposed project.

- If well water is proposed to be the source of water supply for a Subdivision, the final engineering report shall include a well water availability study which shall include comments regarding the long term (30 years) quantity and quality of the available well water supplies relative to the ultimate needs of the Subdivision.

- In any area not controlled by an approved rural water supplier, Developer shall provide written approval from the Texas Commission on Environmental Quality (TCEQ) for the quantity and quality of water to be provided to the proposed Subdivision prior to submittal of the Preliminary Plat

  - Sewer Utilities:

As a condition of Final Plat approval, each Developer of a Subdivision shall provide a letter of authorization/certification from the utility company or companies providing wastewater service to the proposed development, as applicable, certifying that sewer service for the proposed Subdivision complies with all applicable laws and regulations.  Additionally, Developers shall comply with all requirements of applicable Kaufman County Regulations for sewer service for the proposed Subdivision, as well as these Regulations, State and Federal law applicable to wastewater utilities and OSSF, and shall at minimum comply with the following requirements:

- Organized Collection and Treatment Systems:

  - Developers who propose to dispose of wastewater by connecting to an existing permitted facility shall accommodate the total flow anticipated from the ultimate development and occupancy of the proposed Subdivision for a minimum of thirty (30) years.  Engineering plans for the proposed wastewater collection lines shall be approved by the TCEQ prior to construction.

  - Where wastewater treatment capacity is to be provided by a political Subdivision of the State, including a city, municipal utility district, water control and improvement district, nonprofit water supply corporation , or an existing investor-owned water supply corporation, the Developer shall furnish evidence of a contractual agreement between the developer and the governing board of the entity or owner of the utility to the effect that necessary arrangements have been made by the developer and the entity for the provision of sufficient wastewater treatment capacity to serve the ultimate occupancy needs of the Subdivision for a term of not less than thirty (30) years.  Before Final Plat approval, an appropriate permit shall be obtained from the TCEQ, and plans and

  - specifications for the proposed wastewater collection and treatment facilities shall be approved by all entities having jurisdiction over the proposed Subdivision.

  - Where there is no existing entity or owner to construct or maintain the proposed wastewater treatment and collection facilities, the Developer shall establish an investor-owned utility by obtaining a Certificate of Convenience and Necessity from the TCEQ.  Before Final Plat approval, a wastewater treatment permit authorizing the treatment of the wastewater for the ultimate occupancy needs of the Subdivision shall be obtained from the TCEQ and plans and specifications for the proposed wastewater collection and treatment facilities shall have been approved by all entities having jurisdiction over the proposed Subdivision.

- Individual On-site Sewage Facilities:

  - Subdivisions served by On-Site Sewage Facilities shall provide for individual Lots, each with a surface area not less than one (1) acre.  The one (1) acre shall be Useable Surface Area and shall comply with TCEQ OSSF TAC chapter 287, Table 10 separation distances, as amended, and other applicable regulations.

  - On-Site Sewage Facilities not required to obtain a wastewater permit through the TCEQ shall apply for permit through the representative designated by Kaufman County.

  - On-site sewage plans must be submitted and approved prior to installation of the system.

  - The following items shall be provided by Developer prior to the approval of a Final Plat:

    - Development Plan – shall state the overall reason for the Subdivision. (i.e. being developed for General Retail and Industrial District uses, Single Family Lot District, etc.); NOTE:  Are there additional elements that the City wants to have included?

    - Topographic Map;

    - 100-Year Flood Zone;

    - Soil Survey;

    - Location of water wells in the development, or within 150 feet of the development;

    - Location of all Easements;

    - Comprehensive Drainage Plan; and

    - Detailed description of all types of sewage facilities suitable for the soil conditions and restrictions of the proposed development as provided by a registered sanitarian or professional Engineer.

- Permitting for On-Site Sewage Facility or Septic System on Illegally-Subdivided Parcel.

  - No official or employee of the City or County may issue a permit for an On-Site Sewage Facility (“OSSF”) or septic system on any parcel that has been subdivided without meeting the requirements of these Regulations (“Illegally Subdivided Parcel”) as adopted in 1999, 2009 or 2016, 2018 or as amended.  If the owner or agent in control of such an Illegally Subdivided Parcel desires to obtain an OSSF or septic system permit, they shall first comply with the requirements of the Cottonwood City Subdivision Regulations.

  - Nothing in this subsection is intended to create more stringent standards for OSSF or septic systems than those adopted included in Title 30 Texas Administrative Code Chapter 285.  The standards for OSSF or septic systems are subject to state law, including Title 30 Texas Administrative Code, Chapter 285, and Texas Health and Safety Code, Chapter 366, Section 366.032, and other applicable laws and regulations of the State of Texas, and Kaufman County, including the resolution adopted by Kaufman County to become an authorized agent of the TCEQ pursuant to Title 30 Texas Administrative Code Section 285.10.

  - Lots:

    - The minimum Lot size for a single-family dwelling, as authorized in a Single Family Lot District, utilizing individual on-site sewage facilities shall be five (5) acres.

9.08.02	Building Setback Lines be fifty (50) feet from the edge of the Right Of Way along all state or federal Roads and highways.  The Building Setback Lines from all other Streets and Roads shall be twenty-five (25) feet.  Building Setback Lines shall be shown on the Preliminary and Final Plats.  No building or structure shall be permitted in the area between the Building Setback Line and the Street Right Of Way.

9.08.03	Lots shall have minimum Road frontage as indicated by the following:

| Lot Size | Minimum Frontage * |
| --- | --- |
| Greater than or equal to five (5) acres | 275 feet |

* Minimum cord length along a curve, and minimum frontage in cul-de-sacs shall be measured at the Building Setback Line.

9.08.04	All Lots shall abut and have direct access to a County Street or Road or abut and have direct access to a Private or Public Street/Road that has been constructed to the current construction standards of these Regulations, and which has the required dedicated Right Of Way.

    - Panhandle or flag-shaped Lots shall be prohibited, except if approved by the City Council as consistent with the intent and spirit of these regulations. The Developer shall advise the City Council if a proposed Lot constitutes a panhandle or flag-shaped Lot as defined herein, and at its sole discretion, the City Council shall evaluate any problems related to inadequate Road and driveway access, shoulder maintenance, drainage maintenance, addressing, delivery of emergency services, school bus routing, the preservation of adequate sight distance for public safety, and any other relevant factors that may affect surrounding property owners or the public at large in making its final determination as part of the Subdivision process. None of the considerations herein shall be construed as vesting any right to the creation of panhandle or flag-shaped Lots as part of the Subdivision process.  Decisions of the City Council pursuant to this Section shall be at the sole discretion of the City Council and shall be final.

9.09	Floodplains:

9.09.01	Subdivisions that are located in a flood zone as shown on the current Flood Insurance Rate Map (FIRM) for City of Cottonwood and or Kaufman County shall

comply with this Section.  Subdivisions containing a Floodway shall be subject to encroachment review, and Developer shall be required to submit an encroachment

certification by a licensed Engineer.  The Developer shall be responsible for the costs of any engineering studies and certifications necessary to determine the impact of improvements on flood flows downstream, and flood heights upstream and adjacent to the Subdivision.

9.09.02	All Subdivision submittals shall comply with the current Floodplain Management Regulations adopted by the City of Cottonwood Council and/or Kaufman County, as applicable.

9.09.03	The finished floor elevation for each Lot located in the Floodplain shall be shown on the Final Plat, and the boundaries of the Floodplain shall be delineated. The finished floor elevation shall be no less than two (2) feet above the Base Flood Elevation (BFE) for each Lot located in the Floodplain.

9.09.04	The Preliminary and Final Plat shall have a notation stating: “A Floodplain development permit is required from Kaufman County prior to any construction in the Floodplain”.

9.09.05	Permanent type benchmarks shall be set in appropriate locations with the description and elevation shown on the Plat.

9.09.06	All Subdivisions located within, or abutting, any area designated as ZONE A on the current Flood Insurance Rate Map (“FIRM”) for Kaufman County shall provide with the Final Plat a detailed base flood elevation study for the Subdivision at the sole cost of the Developer.

SECTION X

VARIANCES

10.01	Variances.

10.01.01   As expressly authorized in these Regulations, a Developer may request a variance from the requirements of these Regulations, and after public hearing, the City Council may authorize a variance, when the Council determines that the variance requested is in harmony with the general purposes and intent of these Regulations and when the granting of the variance would serve to further the public health, safety and welfare and does not hinder orderly development of property.  When making such

determination, among other factors determined relevant by the City Council, the City Council may consider one or more of the following factors:

(1) The probable effect of such variance upon traffic conditions, drainage, public health, and the safety of the existing and future residents;

(2)  That the granting of the variance will not be detrimental to the public health or safety or injurious to other property in the area;

(3)  That the granting of the variance will not have the effect of preventing orderly division of other land in the area in accordance with these Regulations;

(4)	That there are special circumstances or conditions affecting the land involved such that the strict application of the provisions of these Regulations would deprive the applicant of the reasonable development of the land;

10.01.02  When granting a variance, the City Council may prescribe conditions and grant the variance subject to such conditions that Council deems necessary or desirable for the benefit of the public health, safety, and welfare.   Such findings of the City Council, together with the special facts upon which the findings are based, shall be incorporated into the official minutes of the meeting at which the variance is granted.    The decision of the City Council regarding the approval or denial of a variance shall be final.  An applicant for a variance shall pay all costs associated with the variance request in accordance with the City’s Fee Schedule.

APPENDIX A

Plat Notes for City Officials

Approval by the City of _________________

STATE OF TEXAS

KNOW ALL MEN BY THESE PARENTS:

COUNTY OF _________________

I, (_____________), Mayor of the City of _________________, Texas, do hereby certify that this Final Plat, with field notes hereon, having been fully presented to the City Council of the City of _________________, Texas, and by the Council duly considered, was on this day approved and the Plat is authorized to be registered and recorded in the proper records of the County Clerk of _________________ County, Texas.

_____________________________				__________________

(___________________)					Date

Mayor, City of _________________, Texas

City Approval

Certificate of Compliance

The undersigned, the City Secretary of the City of _________________,  _________________ County, Texas, does hereby certify that on the ______ day of __________, 20___, the _________________ City Council, by appropriate action, did find that this Final Plat is in compliance with applicable City’s  Subdivision regulations, and did approve the same for filing in the Plat records of _________________ County, Texas.

Certified this ____ day _________, 20__.

______________________________

City Secretary

City of _________________, Texas

Acceptance of Dedication of Any Public Ways

Certificate of Acceptance of Dedication

The undersigned, the City Secretary of the City of _________________, Texas, does hereby certify that on the ________ day of _______________, 20___, all the owners of real property described above did execute and deliver unto the _________________ City Council their dedication of all Streets, Alleys, parks, Easements, and other public areas to the public, a copy of which is affixed to the face of this Plat; and the _________________ City Council did, by appropriate minute order, accept the dedication of all Streets, alleys, parks, Easements, and other public areas on behalf of the public.

Certified this ____ day of _______________, 20___.

_______________________________

City Secretary

City of _________________, Texas

Dedication Statement for Privately Maintained Roads

The undersigned owner of the above-described property states and acknowledges that the ______ foot wide strip of land is designated as a private access Easement for the benefit of adjoining landowners only, and that the Road on said Easement is a private Road and not a public, nor a City or County, Road of which all buyers and transferees of adjoining property are hereby notified and shall take notice.

Witnessed my hand on this ______ day of __________________, 20___.

_________________________________

Owner

Attest: _____________________, City Secretary

APPENDIX B Need to edit per changes to widths